## Slide 1
SETU
Hyderabad Monsoon Flood-Risk Model & Japanese Intervention Planner
145 GHMC wards
2020-validated
AI-grounded Q&A
India–Japan Innovation Hackathon

## Slide 2
This isn't a hypothetical pairing
Telangana is already at Japan's door for exactly this kind of infrastructure
2025
Telangana CM Revanth Reddy travels to Tokyo, meets JICA (Japan International Cooperation Agency) leadership directly.
The ask
Financial + technical support for Hyderabad Metro Phase 2 and — critically — Musi River rejuvenation, the city's core flood-management corridor.
Why Japan
A century of monsoon-country flood engineering: retention basins, permeable surfaces, underground storage tunnels — proven at city scale.
SETU answers the natural next question: where in the city, and with which specific method?

## Slide 3
The problem: October 2020
A 1-in-117-year event that overwhelmed the city
192 mm
rain in 24h
at Begumpet (IMD)
9+
deaths across the city
during the flood
~34 km²
documented
inundated area
1-in-117
year event
(RMSI advisory)
Gurram Cheruvu (Balapur lake) bund breach
The single deadliest mechanism — a lake bund failed and submerged the Chandrayangutta/Falaknuma belt. Not every part of the disaster was simple rainfall pooling, and our model is honest about that distinction.

## Slide 4
What SETU does
Three things, in one flow
1
Simulate
Slide rainfall (25–300 mm) and watch flood depth rise, ward by ward, spreading downhill exactly as water would.
2
Recommend
Every flooded ward gets ranked Japanese interventions — cost, build time, impact — matched to what that ward actually needs.
3
Explain
An AI advisor per ward answers free-text questions, grounded in that ward's own precomputed flood data — not a generic chatbot.

## Slide 5
How it's built
Six scripts, one linear pipeline — run once, ship static JSON to the browser
p1
fetch
Pulls the DEM (30m elevation), roads, hospitals, water bodies for Hyderabad from OpenTopography + OSM.
p2
zones
Computes per-ward elevation, slope, ponding fraction, area, and which wards are neighbours — from the raw DEM.
p3
flood
The model. Scores every ward's flood susceptibility, runs rainfall → runoff → drainage → ponding → spill for each scenario, calibrates against 2020.
p4
network
Cuts flooded roads from the network graph; recomputes nearest-hospital distance per ward per scenario.
p5
recommend
Matches each flooded ward's profile against the Japanese intervention library; ranks by fit.
p6
export
Flattens everything into small JSON files the static frontend reads — no server needed except the AI proxy.

## Slide 6
The core formulas
Every ward uses the same equations — nothing is hand-tuned per ward
1 · Flood susceptibility (0–1 per ward)
s = 0.38·water + 0.30·elev + 0.16·slope + 0.16·pond Each term is a percentile RANK (0=safe, 1=worst) across all 145 wards — not a raw number — so every ward is compared on the same scale. • water — closeness to a lake/tank
• elev — how low the ward sits
• slope — how flat it is (flat = pools)
• pond — fraction of ward below its own mean elevation
2 · Per-scenario water balance (per ward)
runoff = rain_mm · area · runoff_c drain = drain_cap · (1.45 − 1.17·s) · area · 6h net = runoff + inflow_from_upstream − drain If net fits in the ward's low ground → it ponds there. If net overflows → the excess spills downhill into the next-lowest neighbouring ward, cascading through the whole city in one elevation-ordered pass. Flooded ⇔ depth ≥ 0.12 m

## Slide 7
Calibration, not guesswork
Two global knobs — runoff_coefficient and drain_capacity — tuned by grid search
The search
Every (runoff_c, drain_capacity) pair is run at 192 mm — the real 2020 rainfall — and scored on how well it reproduces the documented 2020 flooded wards, while penalising any pair that floods an implausible share of the city.
score = 0.50·recall(high-conf) + 0.32·recall(high+medium) + 0.18·precision
recall(high-conf) — did we catch the wards where people died / were rescued? recall(high+medium) — broader documented coverage precision — of what we flood, how much is actually documented (fights false positives)

## Slide 8
Validation against October 2020
Honest numbers — including what we don't catch, and why
Confirmed hit
Model misses
Model flags, unconfirmed
At 192 mm (the 2020 rainfall)
18 documented wards from 2020 news coverage · 9 high-confidence (deaths / rescues) · ~145 wards modelled citywide
The model flags a physically plausible, concentrated flood zone (~20% of the city) — not a city-wide wash — and reports both hits and misses openly rather than hiding them.
Two documented deaths are structural collapses, not floods
Hafeezpet: a house collapsed. Balanagar: a factory wall collapsed. Both deaths happened during the storm — but a ward-level flood-depth model has no way to predict a wall failing. We call this out ourselves: it's a stated scope boundary, not a hidden gap.

## Slide 9
Grounded AI, not a generic chatbot
Every ward has its own advisor, briefed on that ward's own data
How it's grounded
Ask "why this method?", "why was X rejected?", or type a free question.
Every request sends that ward's precomputed profile — elevation, flood depth, nearest hospital, ranked interventions — as context to Groq before it answers.
Answers are grounded in the model's own numbers, not invented on the fly.
Why it's safe
Key stays server-side A small local proxy calls Groq — the API key never reaches the browser. Fails gracefully If the AI is unreachable, the app still shows the full static explanation — only the free-text Q&A pauses. Cheap to demo Groq's inference speed keeps ward Q&A near-instant on stage.

## Slide 10
What we're upfront about
Say these before judges ask
Resolution
Ward-level, not street-level — GHMC's private storm-drain network isn't public data.
Validation sample
18 wards from news coverage, not a full damage survey — purple (unconfirmed) wards are plausible, not proven wrong.
Event type
2020 was partly a tank-bund breach — a different mechanism from everyday rainfall pooling, which is what this model targets.
Intervention effect
A modelled planning-stage estimate, not a hydraulic re-simulation of the fix.

## Slide 11
Live demo
Slide the rainfall. Click a flooded ward. Ask it why.
SETU